## Slide 1: Cracking Wireless Networks
Paul Varoutsos

## Slide 2: DISCLAIMER
This presentation is for informational purposes only.
Attempting to access a network other than your own, or one you have permission to manipulate is illegal in some U.S. jurisdictions. Paul Varoutsos, is not to be held liable for any damages or illegal/unethical activity resulting from the use or misuse of the information in this presentation.

## Slide 3: Contents
Types of Networks
  WEP
  WPA
About WPA
How This Crack Works
An Introduction to Aircrack
Demonstration of a WPA crack

## Slide 4: About WPA
Bssid
Essid
Channel
Authentication and cipher types

## Slide 5: How This Crack Works
Packets
Packets
Access Point
Connected Computer
Problem?
Overwhelm client with packets….
Us

## Slide 6: How This Crack Works
Create a quick denial of service attack (DoS)
Capture a four-way handshake
A client MUST be connected to the access point
Apply a brute force dictionary attack to the handshake.
The dictionary MUST contain the password

## Slide 7: So What Do I Need to Start Messing With My Neighbors?
Knowledge of Linux/Unix (Represent!)
aircack-ng software suite
A Wi-Fi card that supports monitor mode
  Can be tricky.
A large dictionary
Lots of Processing Power
  If manually creating a hash table

## Slide 8: Aircrack-ng: Overview
Commands
  airmon-ng - A Bash script that turns your network card to monitor mode
  airodump-ng – A wireless packet capture tool
  aireplay-ng – Inject packets into a wireless network to generate traffic
    If all else fails, you can use this disconnect people from any wireless network at will
  airolib-ng – Manage and create WPA hash tables
  aircrack-ng – a 802.11 WEP/WPA key cracker

## Slide 9: airodump-ng
A wireless packet sniffing tool
  airodump-ng mon0
    Basic command
    mon0 is the network interface name
  airodump-ng --bssid 00:1B:9E:B2:60:00 -c 1 -w output mon0
    --bssid - Only show the network with the given BSSID
    -c Only listen on channel 1
    -w Output captured data to ./output

## Slide 10: Example
MAC address of the access point

## Slide 11: Example
Signal level as reported by the network card.
Can be used to pinpoint the physical location of an access point!

## Slide 12: Example
Number of beacons the access point sends out.

## Slide 13: Example
Number of captured packets.

## Slide 14: Example
Packets per second (over last 10 seconds)

## Slide 15: Example
Max speed that the access point supports

## Slide 16: Example
Encryption type
WEP = LOL

## Slide 17: Example
Cipher type used

## Slide 18: Example
Authentication protocol used

## Slide 19: Example
The SSID of the access point. May be empty if the SSID is hidden.
(But airodump-ng can figure it out anyway)

## Slide 20: Example
MAC address of each client looking for an access point. If not connected to an access point yet, BSSID is blank.

## Slide 21: Example
Data rate between client and access point

## Slide 22: Example
# of lost packets

## Slide 23: Example
# of packets sent by client

## Slide 24: Example
ESSIDs probed by the client. The network that the client if trying to connect to (if not already connected)

## Slide 25: aireplay-ng
Inject packets into a wireless network
Used to generate traffic for crackin WPA and WEP
aireplay-ng --deauth 10 -a 00:1B:9E:B2:60:00 -c 00:12:17:94:90:0D mon0
  -a Set the acces point MAC address
  -c Set the destination MAC address
--dauth sends deauthentication packets
  Recovers a hidden ESSID
  Forces a client to authenticate

## Slide 26: airolib-ng
Basically just a large SQLite database
Manage and create WPA/WPA2 pre-computed hash tables
Stores ESSIDs and Passwords to create hashes
Hashes are used to brute force the password
airolib-ng crackwpa --import essid ~/essid
airolib-ng crackwpa --import passwd ~/passwd

## Slide 27: aircrack-ng
802.11 WEP/WPA key cracker
Easily cracks WEP after enough packets are captured
  http://eprint.iacr.org/2007/120.pdf
For WPA a dictionary method is used

## Slide 28: WPA Crack Demo…